## Slide 1: Verilog to System Verilog
Prashanth Srinivasa Machavaram 
NCD Baseband Hardware Team, LSI India

## Slide 2: Agenda
Background
Verilog Limitations
System Verilog
  Test bench Features
    Data types
    Classes
    Interfaces and Virtual interfaces
    Arrays and methods
    Randomization
    Communication/Inter-process communication
    Direct Programming Interface
  Design Features
  Assertions
Summary

## Slide 3: Background
Complexity of SoC design and verification
Chart: 
| N | N+2 | N+4 | N+6
Design | 1 | 2 | 3 | 4
Verification | 2 | 4 | 8 | 16

## Slide 4: Verilog Limitations
module testbench (input clk, output rst, output w_r_en,
output [31:0] addr, output [31:0] wdata, input rdata);
task reset;
//drive reset
endtask
task write;
input [31:0] ad, dta;
//Drive address, control and data
endtask
task read;
input [31:0] ad;
output [31:0] dta;
//Drive addr/control and sample data
endtask
task do_write_read;
input [31:0] ad;
output [31:0] value;
write('h12345678, 'habab_cdcd);
read('h12345678, value);
endtask
endmodule
module test_top();
reg clk;
design d(clk, ...);
testbench tb(clk, ....);
//Generate clock
endmodule
module test1;
test_top top();
reg [31:0] data;
initial begin
top.reset();
top.write('h10000000, $random);
top.read('h10000000, data);
top.do_write_read();
end
endmodule

## Slide 5: Verilog Limitations
No/limited randomization features
  Only $random
  Cannot have random sequences easily
Limited Reusability
  Cannot reuse the same BFMs/transactors for all tests (error injection, change in the behavior, etc)
  Cannot have layered test bench, for reuse across projects
Array limitation – only fixed arrays
  Large arrays consume large runtime memory (causing huge initial loading time)
No Functional coverage
No Assertions

## Slide 6: System Verilog – Superset of Verilog 2001

## Slide 7: System Verilog
Test bench Features
  Data types
  Classes
  Virtual interfaces
  Arrays and methods
  Randomization
  Synchronization features
  Direct Programming Interface
Design Features
  Interface, always_ff, always_comb, always_latch, etc
Assertions

## Slide 8: System Verilog – Additional Data types
2-state variables – int, bit
  Lesser memory foot print
Enum
  Good for debugging
  Eg: typedef enum bit[1:0] {READ=0, WRITE=1} my_kind_t;
Structures & Unions
  Similar to C
Classes
Others (logic, shortint, longint, etc)

## Slide 9: System Verilog – Classes
Created and destroyed dynamically
Can have methods (tasks and functions)
Can have random/non-random variables
Data hiding
Inheritance
Polymorphism
Can be Parameterized

## Slide 10: System Verilog – Classes (Construction & Destruction)
module testbench (input clk, output rst, output w_r_en,
output [31:0] addr, output [31:0] wdata, input rdata);
task reset;
//drive reset
endtask
task my_random(transaction tr);
if (tr.kind == transaction::READ) read(tr.addr, tr.data..);
if (tr.kind == transaction::WRITE) write(tr.addr, tr.data..);
endtask
task write;
input [31:0] ad, dta;
//Drive address, control and data
endtask
task read;
input [31:0] ad;
output [31:0] dta;
//Drive addr/control and sample data
endtask
endmodule
module test1;
test_top top();
reg [31:0] data;
initial begin
top.reset();
for (int i=0; i<100; i++) begin
transaction tr = new;
tr.randomize();
top.tb.my_random(tr);
tr = null;
end
end
endmodule
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
local bit value;
endclass
Creation of object
Destruction of the object (optional)

## Slide 11: System Verilog – Classes (Construction & Destruction)
transaction tr;
tr = new();
tr = null;
tr (int)
addr
data
kind
value

## Slide 12: System Verilog – Classes (Methods and data hiding)
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
function new();
$display(“This is the constructor”);
endfunction
virtual function bit [4:0] calculate_ecc();
bit [4:0] ecc;
//calculate ecc value
return (ecc);
endfunction
endclass
Keep the public methods virtual
Variables and methods can be declared public, local or protected
Constructor method gets executed automatically when the object is initialized
Keep public methods virtual

## Slide 13: System Verilog – Classes (Scope resolution)
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
bit config_val;
function new(bit config_val);
int addr = 5;
this.config_val = config_val;
this.addr = 10;
endfunction
endclass
Local scope has the higher priority.
this keyword is required to resolve the scope conflict

## Slide 14: System Verilog – Classes (Inheritance & Polymorphism)
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
virtual function bit [4:0] calculate_ecc();
bit [4:0] ecc;
//calculate ecc value
return (ecc);
endfunction
endclass
class custom_transaction extends transaction;
bit good_cfg;
constraint cst_addr {
if (good_cfg) { addr inside {[0:100]}; }
else { addr inside {[1000:100000]};}
}
function new(bit cfg_val);
super.new();
this.good_cfg = cfg_val;
endfunction
virtual function bit [4:0] calculate_ecc();
bit [4:0] ecc;
if (this.good_cfg) return super.calculate_ecc();
else return (0);
endfunction
endclass
Derived class extends base class and adds its functionality
  Base class method can be re-written
  super.method() can be used to call the base class method
Optional if no arguments

## Slide 15: System Verilog – Classes (Inheritance & Polymorphism)
module testbench (input clk, output rst, output w_r_en,
output [31:0] addr, output [31:0] wdata, input rdata);
task reset;
//drive reset
endtask
task my_random(transaction tr);
if (tr.kind == transaction::READ) read(tr.addr, tr.data..);
if (tr.kind == transaction::WRITE) write(tr.addr, tr.data..);
endtask
task write;
input [31:0] ad, dta;
//Drive address, control, data, ecc, etc
endtask
task read;
input [31:0] ad;
output [31:0] dta;
//Drive addr/control and sample data
endtask
endmodule
module test1;
test_top top();
reg [31:0] data;
initial begin
top.reset();
for (int i=0; i<100; i++) begin
custom_transaction tr = new(0);
tr.randomize();
top.tb.my_random(tr);
end
end
endmodule
Creation of derived object
Assigning derived handle to base handle is valid, But not the other way

## Slide 16: System Verilog – Classes (Inheritance & Polymorphism)
transaction tr;
custom_transaction ctr1, ctr2;
tr = new;
ctr1 = new;
ctr2 = new;
ctr2 = tr; //Causes compile error
tr = ctr1;
ctr2 = tr; //Logically correct,
//but still compiler gives error
$cast(ctr2, tr);
tr
addr
data
kind
addr
data
kind
g_cfg
addr
data
kind
g_cfg
ctr1
ctr2

## Slide 17: System Verilog – Classes (Inheritance & Polymorphism)
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
virtual function transaction copy();
transaction tr = new;
tr.addr = this.addr;
……
return (tr);
endfunction
endclass
class custom_transaction;
bit good_cfg;
virtual function transaction copy();
custom_transaction tr = new();
tr.addr = this.addr;
….
tr.good_cfg = this.good_cfg;
return(tr);
endfunction
endclass
custom_transaction ctr1 = new;
custom_transaction ctr2 = ctr1.copy();
$cast(ctr2, ctr1.copy());
Compiler gives error

## Slide 18: System Verilog – Interface
Interface is a collection of related signals
  Reduces effort
  Avoids connecting to each signal during module integration
Can have tasks/functions and assertions that can be reused.
Interfaces are synthesizable
Provision to define the direction of the signals
BLK1
BLK2
BLK1
BLK2

## Slide 19: System Verilog – Interface (modport)
module testbench (intf .mst iport);
task reset;
//drive reset
endtask
task write;
input [31:0] ad, dta;
//Drive address, control and data
@(posedge iport.clk);
iport.addr <= ad;
iport.data <= dta;
……
endtask
task read;
input [31:0] ad;
output [31:0] dta;
//Drive addr/control and sample data
endtask
endmodule
module test_top();
reg clk;
intf itf(clk);
design d(itf.slv);
testbench tb(itf.mst);
endmodule
interface intf(input bit clk);
wire rst;
wire w_r_en;
wire [31:0] addr;
wire [31:0] wdata;
wire [31:0] rdata;
modport mst(output w_r_en, output addr, output wdata, output w_r_en, input rdata, input clk);
modport slv(input w_r_en, input addr, input wdata, input w_r_en, output rdata, input clk);
endinterface
Modport contains direction

## Slide 20: System Verilog – Interface (clocking block)
module testbench (intf .mst iport);
task reset;
//drive reset
endtask
task write;
input [31:0] ad, dta;
//Drive address, control and data
iport.cb.addr <= ad;
iport.cb.data <= dta;
……
endtask
task read;
input [31:0] ad;
output [31:0] dta;
//Drive addr/control and sample data
endtask
endmodule
interface intf(input bit clk);
wire rst;
wire w_r_en;
wire [31:0] addr;
wire [31:0] wdata;
wire [31:0] rdata;
clocking cb @(posedge clk);
default input #1 output #1;
output w_r_en;
output addr;
output wdata;
input rdata;
endclocking
modport mst(clocking cb);
modport slv(input w_r_en, input addr, input wdata, output rdata, input clk);
endinterface
Clocking block provides synchronization with skews

## Slide 21: System Verilog – Virtual Interface
class testbench;
virtual intf.mst iport;
function new(virtual intf.mst iport);
this.iport = iport;
endfunction
virtual task write(input [31:0] ad, dta);
//Drive address, control and data
iport.cb.addr <= ad;
iport.cb.data <= dta;
……
endtask
virtual task read(input [31:0] ad. output [31:0] dta;
//Drive addr/control and sample data
endtask
endclass
module test_top();
reg clk;
intf itf(clk);
design d(itf.slv);
testbench tb;
initial begin
tb = new(itf.mst);
end
endmodule
Virtual interface is being initialized by passing actual interface
Virtual interface is the way to access interface inside class
  Virtual interface is like a pointer which points to the actual interface

## Slide 22: System Verilog – Arrays
Unpacked Arrays
  Similar to the Verilog-2001 style
  Includes event type and all System Verilog types
  Access includes slices of array and entire array
  Each element stored independent from others
bit a [3:0]; // unpacked array of bits
Packed Arrays
  Only bit-level types (reg, wire, logic, bit), or other packed types
  Multiple dimensions allowed
  Access whole array, bit/part selects, or slices
  Entire array stored as contiguous bits (like a Verilog vector)
bit [3:0] b; // packed array of bits

## Slide 23: System Verilog – Multi Dimensional Arrays
}
bit [a:b] [n:m] [p:q] mem [ t:u] [v:w] [x:y];
Packed 4-byte variable
bit [3:0] [7:0] aa ;
Array of 2 packed 4-byte variables
bit [3:0] [7:0] bb [1:0] ;
Nibble copy
bb[1][2][3:0] = bb[0][1][7:4];
}
Unit
}
Packed
Unpacked

## Slide 24: System Verilog – Dynamic Arrays
Powerful data type for modeling.
The size of the array initialized at runtime using the construction function new.
Efficient use of the memory as per the runtime requirements.
Syntax :
  <Data_Type> <NAME> [ ];
bit [3:0] my_nibble[ ]; // Dynamic array of 4-bit vectors
integer memry[ ]; // Dynamic array of integers
int data_array[ ]; // Declare a dynamic array
data_array = new[256]; // Create a 256-element array
int addr = new[100]; // Create a 100-element array
addr = new[200](addr); // Create a 200-element array by preserving previous
// values in lower 100 addresses

## Slide 25: System Verilog – Dynamic Array Methods
size() – Returns the current size of the array.
int array_size;
int data_array = new[100];
array_size = data_array.size(); // returns 100
delete() – Empties the array contents and size set to zero
data_array.delete();
array_size = data_array.size() ; // returns zero

## Slide 26: System Verilog – Associative Arrays
Powerful data type for modeling SPARSE Memories and CAMs ( indexed Memories).
Efficient use of the memory as it is not required to allocate complete memory. Useful in modeling memories whose size is huge or unpredictable.
Memory Elements can be added and removed individually inside the array.
Pre-defined methods for array accessing.
  num(), delete(), exists(), first(), last(), next(), prev()
Syntax :
  <Data_Type> <ARRAY_NAME> [ index_data_type];
Example:
    bit [7:0] age [string]; // associative array of 8-bit vectors, indexed by string type
    bit [31:0] mem_array[longint] // modelling a sparse memory
    age [“tom”] = 21;
    age [“joe”] = 32;
    $display(“Tom is %d years of age ”, age[tom], “[%d ages in database]”, age.num());
    mem_array[64’h0000_000A_FFFF_AAAA] = 32’h0000_AAAA;

## Slide 27: System Verilog – Queues
A queue is a variable sized array of any data type.
System Verilog queue is an ideal data type to model queues, stacks using the predefined methods.
Syntax :
  <Data_Type> <ARRAY_NAME> [ $];
Example:
    int fifo[$]; // int type fifo
    bit [3:0] nibble[$] ; // nibble list
    int size;
    ………………
    ………………
    size = nibble.$num; //returns size of the list array.
    nibble = {} ; // clear the list array
    nibble = { nibble, 4’h2} ; // add element to right end
    nibble = {4’hf, nibble}; // add element to left end

## Slide 28: System Verilog – Queues Methods

## Slide 29: System Verilog – Randomization
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
bit config_val;
constraint my_cst {
addr > 0;
addr <= ‘habcd_1234;
}
function pre_randomize();
$display(“This is pre-randomize”);
endfunction
function post_randomize();
$display(“This is post-randomize”);
endfunction
endclass
Pseudo-random values get generated with every object.randomize() call.
for (int i=0; i<100; i++) begin
transaction tr = new();
tr.randomize();
$display(“Addr=0x%x, Data=0x%x, kind=%s”,
tr.addr, tr.data, tr.kind.name);
end
end

## Slide 30: System Verilog – Randomization
class custom_transaction extends transaction;
constraint custom_cst {
(kind == READ) -> addr inside {[32’h1000:32’h2000]};
(kind == WRITE) -> addr inside {32’h500, 32’h2000};
addr != 32’h500;
addr != 32’h2000;
kind != READ;
}
endclass
Constraints can be conditional
Ranges and required values can be specified in constraints
for (int i=0; i<100; i++) begin
custom_transaction tr = new();
tr.randomize();
$display(“Addr=0x%x, Data=0x%x, kind=%s”, tr.addr, tr.data, tr.kind.name);
end
end
Causes constraint solver error

## Slide 31: System Verilog – Randomization
class Generator;
rand int val_array[];
rand transaction obj_array[$];
constraint custom_cst {
val_array.size() == 10;
foreach (val_array[i]) {
(i==0) -> val_array[i] == 5;
(i !=0) -> val_array[i] = val_array[i-1] + 1;
}
foreach (obj_array[i]) {
(i==0) -> obj_array[i].kind == WRITE;
(i !=0) -> obj_array[i].kind != obj_array[i-1].kind;
}
}
function new();
for (int i=0; i<2; i++) begin
transaction tr = new;
obj_array.push_back(tr);
end
endfunction
endclass
foreach can be used for providing relation between the array elements
Queue needs to be filled up before randomization

## Slide 32: System Verilog – Randomization
class transaction;
typedef enum bit {READ=0, WRITE=1} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
bit config_val;
constraint my_cst {
addr > 0;
addr <= ‘habcd_1234;
}
constraint my_cst1 {
kind == WRITE;
}
endclass
Constraints can be switched off if required.
Random variables can be made non-random if required
Constraints can be specifed inside object.randomize() with {}
for (int i=0; i<100; i++) begin
transaction tr = new();
tr.addr = 50;
tr.addr.rand_mode(0);
tr.my_cst1.constraint_mode(0);
tr.randomize() with {
data == 32’h5555_5555;
};
end

## Slide 33: System Verilog – Randomization
class transaction;
typedef enum bit {READ, WRITE, EAT, SLEEP} kind_t;
rand bit [31:0] addr;
rand bit [31:0] data;
rand kind_t kind;
constraint my_cst {
addr dist { [32’h5000:32’h10000] :/ 5,
[32’h20000:32’h40000] :/ 2
};
kind dist { [READ:EAT] := 5,
SLEEP := 2
};
}
endclass
Distribution of random values can be controlled by providing weights using dist.
Range gets the weight of 5
Each element gets the weight of 5

## Slide 34: System Verilog – Randomization (Sequential)
int a;
randcase
5: a = 100; //50% probability 5/10
3: a = 10; //30% probability 3/10
2: a = 50; //20% probability 2/10
endcase
randcase – Random selection of the branches with weight
$urandom_range – generates a random integer value with the specified range
randseq – sequences get selected randomly or sequentially
int a;
a = $urandom_range(20, 40); //a gets a value between 20 & 40
randsequence (MAIN)
MAIN : SEQ_1 SEQ_2 SEQ_3
SEQ_1: SEQ_2 | SEQ_3
SEQ_2: SEQ_4 SEQ_5
SEQ_3: $display(“This is sequence 3”);
SEQ_4: $display(“This is sequence 4”);
SEQ_5: $display(“This is sequence 5”);
endsequence
Random sequence selection

## Slide 35: System Verilog – Randomization
class testbench;
function new(virtual intf.mst iport);
this.iport = iport;
endfunction
task my_random(transaction tr);
if (tr.kind == transaction::READ) read(tr.addr, tr.data..);
if (tr.kind == transaction::WRITE) write(tr.addr, tr.data..);
endtask
endclass
module test1;
test_top top();
initial begin
top.reset();
scenario scn = new(5);
scn.randomize();
for (int i=0; i<5; i++) begin
top.tb.my_random(scn.obj_array[i]);
end
end
endmodule
class scenario;
rand transaction obj_array[$];
constraint custom_cst {
foreach (obj_array[i]) {
(i==0) -> obj_array[i].kind == WRITE;
}
}
function new(int num_items=2);
for (int i=0; i<num_items; i++) begin
transaction tr = new;
obj_array.push_back(tr);
end
endfunction
endclass

## Slide 36: System Verilog – Synchronization/Inter-process communication
Concurrency (fork-join)
Events
Mailbox
Semaphore

## Slide 37: System Verilog – Synchronization/Inter-process communication
fork
begin
#10 $display(“This is Thread 1”);
end
begin
#50 $display(“This is Thread 2”);
end
#100 $display(“This is Thread 3”);
join_all
$display(“Out of fork”);
fork
begin
#10 $display(“This is Thread 1”);
end
begin
#50 $display(“This is Thread 2”);
end
#100 $display(“This is Thread 3”);
join_any
$display(“Out of fork”);
disable fork
fork
begin
#10 $display(“This is Thread 1”);
end
begin
#50 $display(“This is Thread 2”);
end
#100 $display(“This is Thread 3”);
join_none
$display(“Out of fork”);
Executed only after all threads are done
Executed if any one of the threads are done
Executed without waiting for any of the threads
Kills all the threads in the current scope
Concurrency

## Slide 38: System Verilog – Synchronization/Inter-process communication
Events – 2 types of waiting
event evt1, evt2;
fork
begin
#10 -> evt1; //triggering an event
-> evt2;
end
begin
@(evt1) ;
@(evt2);
end
join
Unblocks if executed before event trigger
event evt1, evt2;
fork
begin
#10 -> evt1; //triggering an event
-> evt2;
end
begin
@(evt1) ;
wait (evt2.triggered);
end
join
Unblocks for the whole simtime of trigger
wait (a==5 && b);
Wait can be used for expressions too

## Slide 39: System Verilog – Synchronization/Inter-process communication
Mailbox – Communication between 2 processes
mailbox mbox = new;
fork
begin
repeat (5) begin
mbox.put(1000);
#10;
end
end
begin
int val;
repeat (5) begin
mbox.get(val);
end
end
join
mailbox#(transaction) mbox = new;
fork
begin
repeat (5) begin
transaction tr = new;
tr.randomize()
mbox.put(tr);
#10;
end
end
begin
transaction tr;
repeat (5) begin
mbox.get(tr);
end
end
join

## Slide 40: System Verilog – Synchronization/Inter-process communication
Semaphore – controlling the processes (with the specified num of keys)
semaphore sem = new(1);
fork
begin
repeat (5) begin
sem.get();
do_task1();
sem.put();
end
end
begin
repeat (5) begin
sem.get();
do_task2();
sem.put();
end
end
join

## Slide 41: System Verilog – DPI
DPI – Direct Programming Interface
System Verilog new foreign language Interface.
A simple, straightforward, and efficient way to connect SV and C models.
SV task or function can directly call a C function and vise-a-versa.
The functions implemented in C and used in SV are called imported functions. The C function name is imported into the SV language using an import declaration through DPI interface.
The task or function implemented in SV and used in C function is an exported task or function. The SV task or function name is specified in an export declaration through DPI interface.

## Slide 42: System Verilog – DPI Import
Every imported C function must be declared using an import declaration in SV code.
  import {“DPI” | “DPI-C”} [context | pure] [c_identifier =] function function_data_type function_identifier ([tf_port_list]);
Example:
  import “DPI-C” function int calc_parity (input int a);
Specifying local name to C function in SV. In the following example, the calc_parity_func C function is given the name calc_parity in SystemVerilog
  import “DPI-C” calc_parity_func = function int calc_parity (input int a);
Pure function output dependent only on the input arguments
  import “DPI-C” pure function int calc_ecc(input int data);
Context function output dependents not only on function arguments but also SV variables not specified as arguments
  import “DPI-C” context task calc_task(input int in1, output int out1);

## Slide 43: System Verilog – DPI Export
Every exported SV function must be declared using an export declaration in SV code.
  export {"DPI" | “DPI-C”} [c_identifier = ] function function_identifier;
  export {"DPI" | “DPI-C”} [c_identifier = ] task task_identifier;
C function using the SV function or task needs to include a dpi header file with function declaration.
Example:
  export “DPI-C” my_cfunction = function myfunction;

## Slide 44: System Verilog – DPI Example
#include <stdio.h>
#include "my_header.h"
void RunTest() {
int i,j;
printf("Hello LSI\n");
cfunc_end_test();
}
module test;
import "DPI-C" pure function void RunTest();
export "DPI" cfunc_end_test = function end_test_call;
initial
begin
RunTest(); // C function called in SV
$finish;
end
function void end_test_call();
$display ("end of test\n");
endfunction : end_test_call
endmodule
#include "svdpi.h"
#ifdef __cplusplus
extern "C" {
#endif
extern void cfunc_end_test();
#ifdef __cplusplus
}
#endif
vcs -sverilog test.sv ./RunTest.c
./simv
Header file
C file
SV File

## Slide 45: System Verilog – Missing topics
Functional coverage
Assertions
Design features
Program block
Static methods and variables in classes
Automatic/static scope
Process scheduling
Parameterized classes
Many more 

## Slide 46: Thank You